## Slide 1: Simulation Tool Benchmarking and Verification
Technical Workshop on Fuel Cycle Simulation
Brent Dixon
Idaho National Laboratory

## Slide 2: FCS Verification – What to test
Basic features or essential functionalities
  These are the building blocks of the code
  May also be considered “core capability” blocks
Integral features that bind the basic features together and produce useful results
  Considering the core capabilities as an integrated whole
  Produces a complete result
  Limited to basic capabilities common to most codes
Exemplary features that enable study of particular sensitivities or other capabilities
  May not be present in every tool
  Provides “full features” of a code

## Slide 3: FCS Verification – How to test
General Approaches
  Manual verification of individual equations up to a highly simplified model
  Spreadsheet verification of a simple model
  Benchmarking of single or multiple scenarios with a set of codes
  Auto-verification of code functions/methods
Scenario-Specific Approaches
  Manual or spreadsheet verification of key results
  Cross-comparison to results from other FCS codes

## Slide 4: Unit Tests – Parts of Code or Full Code
Parts example
  Enrichment module provides correct NU, LEU, DU masses and SWUs
Full Code Examples
  Run one reactor at steady state
  Startup and run (and retire) one reactor
  Run a homogenous fleet at steady state
  Run a homogenous fleet with simple growth
Items reviewed in full code tests are just the basics
  Number of reactors, basic material flows
  May omit mining, conversion, transportation, storage, reprocessing, waste disposal, etc.
  Includes no exemplary features such as decay

## Slide 5: Code to Code Testing
Purpose is to produce exactly the same results or be able to explain any differences
Reference result may be calculated with a different tool (e.g. spreadsheet)
Differences may result in:
  Evolution of the specification to eliminate multiple interpretations
  Changes to codes to correct any errors discovered
  Detailed explanation of differences due to different code architectures, time steps sizes, reporting times (e.g. first of the year vs. end o the year), rounding, etc.

## Slide 6: Benchmarking
Full code tests
  May be based on one or a family of scenarios
  Typically will assess more parameters that a code-to-code test
  Often used to prove a new code is ready for production work
  Purpose is typically to produce similar behavior, not exact matches
    Only significant differences require explanation
    Typically these trace back to unmodeled features in less mature codes, etc.
  May involve disabling exemplary features to improve matches
  May be blind or open
    Blind tests do not allow for iteration of the specification if found to allow multiple interpretations

## Slide 7: Benchmarking Examples
MIT Benchmark (2009)
  Included multiple scenarios
    One iterated for close matches with advanced features disabled
    Others allowed for all features to operate, including automated decision-making
  Four mature codes compared

## Slide 8: Benchmarking Examples
NEA/OECD Benchmark (2012)
  Involved a single scenario with three stages
  Five mature codes were compared

## Slide 9: Benchmarking Examples
IAEA/INPRO GAINS (2013)
  Involved three simple scenarios
  Six codes compared (several not previously benchmarked)

## Slide 10: Benchmarking Observations
Results are more understandable with simple scenarios and tight specifications
  Must design around the intersection of code capabilities, not the union
Expect differences in results
  Just because results do not match, does not mean one code is “wrong”
However - Allow time for iterations
  When running a new type of problem, a code may reveal a bug that needs fixing
Expect strong similarities in general trends
  A transition may not occur in the same year, but should occur near the same time
  A slope may not be equal, but should be close (e.g. all trending slightly up)
Use the experience to improve your code
  Tune up your calculations or add a new capability you saw in another code

## Slide 11: References
[1] Brown, N.R., B.W. Carlsen, B.W. Dixon, B. Feng, H.R. Greenberg, R.D. Hays, S. Passerini, M. Todosow, A. Worrall, “Identification of fuel cycle simulator functionalities for analysis of transition to a new fuel cycle”, Annals of Nuclear Energy 96 (2016) 88-95, 2016.
[2] Feng, B., B. Dixon, E. Sunny, A. Cuadra, J. Jacobson, N.R. Brown, J. Powers, A. Worrall, S. Passerini, R. Gregg, “Standardized verification of fuel cycle modeling”, Annals of Nuclear Energy 94 (2016) 300-312, 2016.
[3] Guerin, L., B. Feng, P. Hajzlar, B. Forget, M.S. Kazimi, L. Van Den Durpel, A. Yacout, T. Taiwo, B.W. Dixon, G. Matthern, L. Boucher, M Delpech, R. Girieud, M. Meyer, “A Benchmark Study of Computer Codes for System Analysis of the Nuclear Fuel Cycle”, Center for Advanced Nuclear Energy Systems, Massachusetts Institute of Technology, MIT-NRC-TR-105, April 2009.
[4] “Benchmark Study on Nuclear Fuel Cycle Transition Scenarios Analysis Codes”, Expert Group on Fuel Cycle Transition Scenario Studies, Nuclear Energy Agency, NEA/NSC/WPFC/DOC(2012)16, Paris, June 2012.
[5] “Framework for Assessing Dynamic Nuclear Energy Systems for Sustainability: Final Report of the INPRO Collaborative Project GAINS”, International Atomic Energy Agency, NP-T-1.14, Vienna, 2013.
[6] Gidden, M., Scopatz, A., Wilson, P., “Developing standardized, open benchmarks and a corresponding specification language for the simulation of dynamic fuel cycle”, Trans. Am. Nucl. Soc. 108, 127–130, 2013.

## Slide 12: Discussion
What issues have you encountered in code verification?
What have you been surprised to find or learn?
What weaknesses in current approaches have you noted and what ideas do you have to address them?