## Slide 1: Fuel Composition Transition Modeling
Technical Workshop on Fuel Cycle Simulation
Ross Hays
Idaho National Laboratory

## Slide 2: The Dilemma
We need to model a two-stage recycling reactor scenario
  Stage 1
    High breeding ratio
    Long fuel residency time
    Lower burnup
  Stage 2
    Low breeding ratio
    Shorter fuel residency
    Higher burnup
The reactor transitions between cores gradually, without shutting down
Previous versions of VISION could not do this.

## Slide 3: Background
VISION tracks fuel mass through various fuel cycle stages
Isotopics can be calculated
  Implicitly (total mass at fixed composition)
  Explicitly (individually tracked/decayed)
Buffers for different stages
  Mining, Conversion, Enrichment
  Reactor
  Storage
  Reprocessing, Fabrication
  Disposal
  Etc.
Flows move material from buffer to buffer

## Slide 4: Modeling Fuel in Reactors
Within the reactor module, VISION now:
  Uses recipe-based isotopics
  Tracks fuel in integer bits per timestep (one per reactor)
  Has an index for Fuel Vintage
    Two values: New, Previous
    Can change fuel recipe w/o reactor restart
  Irradiation advancement only for fully fueled reactors
  Improved discharge/advance prioritization
    Previous recipe
    Earliest pass
  Improved discharge calculations
    Surplus fuel (due to shortened irradiation time)
    Shutdown discharge (can be made burnup dependent)
    Refueling discharge
Notes: During a transition from long-irradiating fuel to short, some short-burning fuel will reach discharge time while the reactor still has partially burned fuel from the previous recipe within the reactor. This fuel must be discharged early so that the reactor does not have more than a full load of fuel. (Interpolation between discharge times is not performed, as it is expected to be more complex than warranted for these scenarios).

## Slide 5: Modeling Fuel in Reactors
Flow Diagram (Simplified)
Time in Reactor
New Recipe
Previous Recipe

## Slide 6: Example
Transition through six sequential fuel recipes
  Pass 0 is externally derived
  Pass 1, 2 are recycled transition stage recipes
    High breeding
    5.5 year irradiation time
  Pass 3, 4, 5 are recycled equilibrium stage recipes
    Low breeding
    4.5 year irradiation time
Lower pass material utilized preferentially when available
  Prevents accumulation of low-pass material
  Prolongs evolution to equilibrium in some systems
Pass 0 can be used anytime as a backstop supply

## Slide 7: Example (Startup)
Feed
Discharge
Notes: Reactors start fully fueled with Pass 0 fuel.

## Slide 8: Example (Midway)
Notes: As fuel is recycled, higher passes become available and are loaded

## Slide 9: Example (Transition to Equilibrium)
Pass 3+ discharged at 4.5yr
Pass 2- discharged at 5.5yr
Notes: Pass 3 and higher fuel has a shorter irradiation time than Pass 2 and lower.
Once a reactor has fully irradiated Pass 3 fuel, any remaining Pass 2 or below is discharged.
This is a modeling approximation of how a core might transition from one core loading to another.

## Slide 10: Example (More Transition)
Notes: Transition continues

## Slide 11: Example (Near Equilibrium)
Notes: All reactors are now on Pass 3+ fuel.
Lower pass fuel continues to be fed as full recyclable batches become available.

## Slide 12: Observations
Integers are easier to manage than floats
Book-keeping is straight-forward, until upset conditions must be included. What-if’s include:
  Fuel supply shortage
  Coincident shut-down or startup

## Slide 13: Discussion
What issues have you encountered in extending a model?
What have you been surprised to find or learn?
How would you change things if starting from scratch?
Which assumptions are the most limiting to the results?
Which are the most easily generalized within a the model?
How should one handle the first core load, where batches are not fully irradiated at discharge, and do not require full equilibrium fissile loading?

## Slide 14: Supplemental Material

## Slide 15: Modeling Fuel in Reactors
Previous versions of VISION tracked total mass by
  Reactor type
  Recycling pass
  Irradiation timesteps
There were several drawbacks
  Floating point underflow errors
  Poor handling of fuel supply shortfalls
  Irradiation time, batch sized fixed for each reactor
An improved method was needed